## Slide 1: NanoObejectDetection
Parameter Decision Tree for new Data

## Slide 2: Enhance SNR
Is the particle CLEARLY visible in front of the background?
  Yes: EnhanceSNR = 0  use data as it is
  No: EnhanceSNR = 1  reduce noise by lowpass filter
    Make the image a little bit thicker (approx 20px) more, sothat the filtering can operate with high quality

## Slide 3: ZNCC_min
ZNCC: Zero normalized cross correlation
  Expensive function for feature finding according to
  Value maximal 1 for perfect shape match. Impossible to achieve with noise
Is the particle CLEARLY visible in front of the background?
  Yes: ZNCC_min = 0.7
  No: ZNCC_min = 0.5
    Empirically value used in the 9 nm NP measurements